## Slide 1: Translation Stage System
masi@ihep.ac.cn
TAO SiPM mass testing

## Slide 2: Devices of TSS
Device | Type | Number | Work temperature
slide-rail | VC60-200-5 | 2 | -50˚C ~ 85˚C
step motor | HS5776A-FK | 2 | 
encoder |  | 2 | 
decoder | HFT (12bit) |  | room temperature
driver | HD265 | 2 | 
controller | MRC | 1 | 
decoders
controller
& drivers
X-rail
encoders
motors
Y-rail

## Slide 3: Device Introduction
Controller & driver
  Control the movement of two motors in sequence.
  Driver subdivision can be set to determines the number of pulses required for one cycle. Now the subdivision is set to 1600pulses/cycle.
Decoder
  Used to check the real position of the carrier.
  Value range:
    [0, 4095] for one cycle
    (-2147483648, 2147483647) for cycles

## Slide 4: Data transmission
Between controller and computer
  RS232 serial communication
Between decoder and computer
  RS232 serial communication

## Slide 5: TSS control & monitoring software
PyQT5-based development
  Requires: python 3.9 or later, pyserial, pyqt5
The software provides two user interaction modes:
  Graphic user interface (GUI) interact mode
    Easy to use
  Command line interact mode
    Efficiently to integrate

## Slide 6: TSS GUI

## Slide 7: Additional instructions ---MRC(1)
Front View:
2.8 inch touchable LCD screen
Real time display current position, initial velocity, acceleration and final velocity
Provide 4 shortcut keys, forward, backward, run and return to zero
  Forward: for each press, advance 10000 pulses
  Backward: for each press, go back 10000 pulses
  Return to zero
  Run: run the program, which already stored in flash.
Rear View:
Power Switch
220v power socket
X-axis motor and hardware limit switch interface
RS232 communication and hardware IO output interface

## Slide 8: Additional instructions ---MRC(2)
X-axis motor and hardware limit switch interface diagram
RS232 communication and
hardware IO output interface diagram

## Slide 9: Additional instructions ---Motor
Motor and driver,
encoder and decoder wiring diagram